## Slide 1: EECS 370
DIGITAL LOGIC REVIEW SESSION
Austin Maliszewski
Branden Ghena
Slides heavily borrowed (stolen) from
V. Bertacco,
R. Dick,
T. Austin,
S. Mahlke,
K. Sakallah &
F. Vahid

## Slide 2: Agenda
Lots more slides than we have time to talk about!
  But they’ll go online for your reference.
Quick review of lots of things:
  Transistors
  Gates
  Important Combinational Circuits (decoders/muxes)
  Adders (RCA/CLA)
  Sequential elements (latches/flip-flops)
  The Single Cycle LC-2K (ever so briefly)
  FSMs
  IEEE Floating Point
Your questions!

## Slide 3: The CMOS Transistor
CMOS transistor
  Basic switch in modern ICs
does not
conduct
0
conducts
1
gate
nMOS
does not
conduct
1
gate
pMOS
conducts
0
Silicon -- not quite a conductor or insulator:
Semiconductor
2.3
a
gate
sou
r
ce
drain
o
xide
A positive
voltage here...
(
a
)
IC pa
c
kage
IC
...attracts electrons here,
turning the channel between
the source and drain into
a conductor

## Slide 4: Logic Gates
NOT
AND
OR
XOR
NAND
NOR
XNOR

## Slide 5: More Gates
NAND: Opposite of AND (“NOT AND”)
NOR: Opposite of OR (“NOT OR”)
XOR: Exactly 1 input is 1, for 2-input XOR. (For more inputs -- odd number of 1s)
XNOR: Opposite of XOR (“NOT XOR”)
2.8
x
0
0
1
1
y
0
1
0
1
F
1
1
1
0
x
y
F
x
0
0
1
1
y
0
1
0
1
F
1
0
0
0
x
y
F
NOR
NAND
x
0
0
1
1
y
0
1
0
1
F
0
1
1
0
XOR
x
0
0
1
1
y
0
1
0
1
F
1
0
0
1
XNOR
1
0
x
y
F
x
y
1
0
x
x
y
y
F
NAND
NOR
NAND same as AND with power & ground switched
  nMOS conducts 0s well, but not 1s (reasons beyond our scope) – so NAND is more efficient
Likewise, NOR same as OR with power/ground switched
NAND/NOR more common
AND in CMOS: NAND with NOT
OR in CMOS: NOR with NOT
a

## Slide 6: Controller Components
Decoder
  What does it do?
IN | OUT
000 | 0000_0001
001 | 0000_0010
010 | 0000_0100
011 | 0000_1000
etc. | …

## Slide 7: Decoder Circuit
Symbol:

## Slide 8: Controller Components
Multiplexor (MUX)
  What does it do?
    OUT = (select) ? IN1 : IN2

## Slide 9: Multiplexer (Mux)
A mux is a digital switch
The output copies one of n data inputs, depending on the value of the select inputs
Implementation:
Product terms are mutually exclusive!

## Slide 10: Binary Addition
How do we add two binary numbers?
Just like elementary school!
If we have a fixed number of bits (which is usually the case), a carry out of the most significant column indicates that there’s not enough bits to hold the sum value. This case is referred to as overflow.

## Slide 11: Addition Implementation
Addition of two 1-bit binary numbers, A and B – requires two output bits, which we’ll call S (sum) and C (carry).
XOR Operation
Implementation:
This circuit is called a Half Adder (HA)

## Slide 12
What if we want to add larger numbers?
  What’s missing from HA?
  Need to add carry-in (Ci) input!

## Slide 13
Final Circuit:
This circuit is called a Full Adder (FA)
After all that design work, we really just have 2 HAs with an OR gate
To make an n-bit adder, simply cascade Full Adders to make a Ripple Carry Adder:
A
B
S
Ci
Co
A0
B0
S0
A
B
S
Ci
Co
A1
B1
S1
A
B
S
Ci
Co
A2
B2
S2
A
B
S
Ci
Co
A3
B3
S3
FA
FA
FA
FA
C0
C1
C2
C3
C4

## Slide 14: Carry Look-Ahead Adder
A
B
S
C
p
g
Full
adder
X
G
P
C
G0
P0
C0
Y
G1
P1
C1
14
EECS 370: Introduction to Computer Organization

## Slide 15: 8-bit Carry Look-ahead Adder
X
0 1 0 0 1 0 1 1 1 0 1 1 0 0 1 1
X
X
X
X
X
X
X
Y
0 0 1
0
Carry
0
Y
Y
0 0 1 1 1 0
1 0
Y
Y
Y
Y
0 1 0 0 1 1 0 1 1 0 0 1
0 1 1 1
0
1
0
1
1
1
1
0
1 1 0 1 0 0 1 0
0 0 1 1 1 1 0 1
+ 1 0 0 1 0 1 0 1
1 1 0 1 0 0 1 0
1
0
1
0
0
1
15
EECS 370: Introduction to Computer Organization

## Slide 16: SR (Set-Reset) Latch
S | R | Q | QB | Function
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
Cross-Coupled NOR Gates

## Slide 17: SR Latch Timing
S | R | Q | QB | Function
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 

## Slide 18: D (Data or Delay) Latch
D | Q | QB | Function
0 |  |  | 
1 |  |  | 

## Slide 19: Clocked Level-Sensitive D Latch

## Slide 20: Edge Triggered D Flip-flop
Want a device that will sample its inputs only once per clock cycle
Indicates edge-trigged behavior
“Double-door” analogy

## Slide 21
Pull light switch revisited: D flip-flop implementation
Only one light toggle per clock cycle!
This device is known as a toggle flip-flop

## Slide 22: Why Clocked Logic?
Clocking specifies a time by which all combinational operations are “done”.
What happens in between doesn’t matter.
  This is super important.

## Slide 23: AN Example of Why This matters
Delays in combinational circuits are very real. Here’s an example with a ripple carry adder.

## Slide 24: An Example of why this matters
Let’s zoom in on the interesting part.
The value of a goes from 7 to 1 here

## Slide 25: An Example of why this matters
Let’s zoom in on the interesting part.
There’s propagation delay before the adder even starts to change values.

## Slide 26: An Example of why this matters
Let’s zoom in on the interesting part.
The value stabilizes

## Slide 27: An Example of why this matters
Let’s zoom in on the interesting part.
The next clock edge comes along

## Slide 28: An Example of why this matters
Let’s zoom in on the interesting part.
The latch opens up
(and shows new value)
The flip-flop grabs new value.

## Slide 29: An Example of why this matters
Let’s zoom in on the interesting part.
B changes now,
while the clock is still high.

## Slide 30: An Example of why this matters
Let’s zoom in on the interesting part.
Again, there’s propagation delay before the adder starts to change.

## Slide 31: An Example of why this matters
Let’s zoom in on the interesting part.
The value in the latch changes too!

## Slide 32: An Example of why this matters
Let’s zoom in on the interesting part.
The next falling edge comes along

## Slide 33: An Example of why this matters
Let’s zoom in on the interesting part.
The adder stabilizes.

## Slide 34: An Example of why this matters
Let’s zoom in on the interesting part.
The latch locked with the wrong value!

## Slide 35: An Example of why this matters
Let’s zoom in on the interesting part.
The next positive edge comes along

## Slide 36: An Example of why this matters
Let’s zoom in on the interesting part.
Flip-flop grabs new value
Latch opens again

## Slide 37: Single CYCLE CPU

## Slide 38: Finite State Machines
An abstract machine that can be in one of a finite number of states at a time.
Transitions between states occur based on input.
  For each state, a transition matrix is defined that determines which state is next based on the input.
Usually implemented in hardware with numbered states, and using D Flip-flops

## Slide 39: A Simple FSM
You’ll see this again later…
Implemented as a two bit counter:
  Increments on T
  Decrements on NT (not T)
00
01
10
11
http://en.m.wikipedia.org/wiki/File:Branch_prediction_2bit_saturating_counter.gif

## Slide 40: ARITHMETIC LOGIC UNIT
Schematic Diagram

## Slide 41: ARITHMETIC LOGIC UNIT
Schematic Diagram
Implementation
~&

## Slide 42: IEEE Floating point format (single precision)
Sign bit: (0 is positive, 1 is negative)
Significand: (also called the mantissa; stores the 23 most significant bits after the decimal point)
Exponent: used biased base 127 encoding
  Add 127 to the value of the exponent to encode:
  -127  00000000 1  10000000
  -126  00000001 2  10000001
  … …
  0  01111111 128  11111111
How do you represent zero ? Special convention:
  Exponent: -127 (all zeroes ), Significand 0 (all zeroes), Sign + or -
42
EECS 370: Introduction to Computer Organization

## Slide 43: Floating point Addition
Shift smaller exponent right to match larger.
Add significands
Normalize and update exponent
Check for “out of range”
43
EECS 370: Introduction to Computer Organization

## Slide 44: More or less precision and range (continued)